## Slide 1: Research Methods and Techniques
John Morris
KRIS, King Mongkut’s Institute of Technology Ladkrabang
previously
Faculty of Engineering, Mahasarakham University Computer Science/ Electrical and Computer Engineering,
The University of Auckland
Iolanthe II leaves the Hauraki Gulf under full sail –
Auckland-Tauranga Race, 2007
Measurements and Errors

## Slide 2: MEASUREMENTS and ERRORS

## Slide 3: Measurement Error
Any measurement of a value, x, has two components
  xmeasured = xtrue + e
  xtrue - true value of the quantity measured
  e - measurement error
Measurement error has two components
  Systematic error, es
  and
  Random error, er
  e = es + er

## Slide 4: Measurement Error - Systematic
Systematic error or bias
  Generally
    fixed value and
    same sign for each measurement
    under the same conditions
    eg temperature expands or contracts a rule but the error will be the same at any given T
  Caused by systematic faults or deviations in the measuring device or system, eg
    End effects – zeroes on rulers or meters
    Meniscus of a liquid
    Slippage between wheel and tachometer or odometer
    Inertia of rotating sensors, eg anemometers, flow meters
    Temperature affecting length of a rule or volume of a fluid

## Slide 5: Measurement Error - Systematic
Systematic error or bias
  but can include
    Loss of data or inputs
      eg loss of responses to a survey
      Spoilage of data
    Accidental duplication of data
    Errors reading data
      Mistakes by automated form reader
      Counting people (or anything else) in images
Note
  You might choose to combine all factors like this
  Consider as random errors
    Some positive, some negative

## Slide 6: Measurement Error - Systematic
If the end is not machined carefully
or worn
End error
Zero error
Object being measured
Then placing this ruler against an edge will lead
to a length longer than the correct one –
A systematic error

## Slide 7: Measurement Error - Systematic
End error
Zero error
Object being measured
Then placing this ruler against an edge will lead
to a length longer than the correct one –
A systematic error
If the end is not machined carefully
or worn
91mm
instead of 90mm

## Slide 8: Measurement Error - Systematic
Meniscus in a liquid
Volume is usually read from the
bottom of the meniscus -
Ignoring the volume above it!
Read here
Ignore this
In precise work, the cylinder is calibrated to allow for the water meniscus!

## Slide 9: Measurement Error - Systematic
Water
Mercury
But ..
For some liquids, the
meniscus is convex!
This would lead to a systematic error if you try to measure the volume of such a liquid in a cylinder
calibrated for water!

## Slide 10: Measurement Error - Systematic
Mechanical measuring devices have inertia
Usually won’t ‘start’ with small flows, etc
Leading to zero offset error .. A systematic error
Rotating paddle wheel
Usually with small magnet in one vane
Hall effect sensor here
Sends pulses to counter and timer circuit
Sensor built into pipe
to measure flow rate

## Slide 11: Measurement Error - Systematic
Systematic error or bias
Corrected by calibration
  Simple ‘offset’ errors (end effects) are easily removed by careful calibration
    Small deviation is added or subtracted from each measurement
    eg a compass does not point to true North because of local deviations in the Earth’s magnetic field
    These are available as corrections (called magnetic deviation) to a compass reading on maps
      Especially marine charts!
      Modern GPS systems may be making these corrections less obviously needed 
    Deviation is simply added or subtracted from the actual reading to get the true reading

## Slide 12: Measurement Error - Systematic
Systematic error or bias
Corrected by calibration
  Incorrect or poor calibration also leads to systematic errors!
  eg the flow rate of a liquid is determined by measuring the frequency of pulses emitted by a paddle wheel
  flow = c f
  where f is the frequency in Hz and c the calibration factor
  A calibration procedure gives
  c = 5.5 m3/s/Hz
  when the correct value is
  c = 5.0 m3/s/Hz
  All measurements are systematically high by 10%

## Slide 13: Measurement Error - Systematic
Systematic error
Corrected by calibration
  Incorrect models also lead to systematic errors!
  eg for the paddle wheel flow meter, flow is assumed to be linear with frequency
  flow = c f
  Actually, the relationship is only approximately linear
  Deviations are systematic errors
  In this case, accuracy can be improved by using an empirical model – the actual calibration points
Flow rate
Frequency
Linear model
Measured
Note the ‘end error’ here!
The paddle wheel doesn’t rotate at all until the flow reaches a minimum value

## Slide 14: Measurement Error - Systematic
Quantum effects
  Always remember: measuring a system perturbs it!
Ammeters and voltmeters have internal resistance
  Presence of the meter may drop the voltage across the device
  or
  reduce the current it draws
These are systematic errors
  Correctable if source impedance and internal resistance of meter is known
A
Device
Constant V
source
dV
V-dV
V
Device
Current limited
source
dA
A-dA

## Slide 15: RandOM ERRORS

## Slide 16: Random errors
Almost all measurements have random errors
  Even ‘counting’ exercises such as
    Census of population
      On the census ‘day’
        Some people are missed
        Some are counted twice
        Some more are born
        Some die
      Leading to some deviations from the ‘correct’ value
      Taking another census will involve a different set of ‘errors’
      Every time we count, we will get a new value
        Sometimes larger, sometimes smaller ..
The deviations are random errors

## Slide 17: Quick Test
You do an experiment on students in a class
      You want to measure % of students who remembered yesterday’s class
      So far, 23 students in a class of 31 showed good memory (or paid attention)
      Today, it is raining, so some students miss the class
      Next 3 days are expected to rain too
      Will this introduce a random? Or a systematic error?
  Reporting your experiment
    % of students with good memories is
      So you report 74.193% have good memories
      Correct or not?
      Next day, a new student (with a good memory) enrols
      Now good memory % is

## Slide 18: Quick Test
You do an experiment on students in a class
      You want to measure % of students who remembered yesterday’s class
      So far, 23 students in a class of 31 showed good memory (or paid attention)
      Today, it is raining, so some students miss the class
      Next 3 days are expected to rain too
      Will this introduce a random? Or a systematic error?
  Reporting your experiment
    % of students with good memories is
      So you report 74.193% have good memories
      Correct or not?
      Next day, a new student (with a good memory) enrols
      Now good memory % is
      Now you report 77.419% have good memories ?
      Comment?

## Slide 19: Random errors
Parallax error reading a ruler
  Minor changes in the observer location
  Different readings
Note
Good experimental design will minimize these errors but never eliminate them!
  In this case,
  Place the ruler closer to the pointer
  or
  Fix the observer’s position with an aperture
  or
  Place a mirror behind the pointer
All of these will reduce random errors,
but
some will remain!

## Slide 20: Random errors
Key property of random errors is their distribution
If you can model processes causing errors, then
  you can estimate how errors will be distributed and
  how to best estimate the true value of the variable you are measuring
However, this is often hard or impractical
  Real physical systems are complex and have many variables
So we commonly assume that random errors will be normally distributed
This is empirically justified in many situations
  But there are some exceptions .. See later
Theoretical support comes from the central limit theorem

## Slide 21: Normal distribution
We have a measurement, xmeasured = xtrue + e
We’ll assume that
    systematic errors have been removed from xmeasured by calibration and
    e represents random errors only.
If we know how e is distributed, we can infer a value for xtrue and its likely error

## Slide 22: Error Distribution
We have a measurement, xmeasured = xtrue + e
We’ll assume that systematic errors have been removed from xmeasured by calibration and that e represents random errors only
If we know how e is distributed, we can infer a value for xtrue and its likely error
Normally distributed errors have a probability function
where m is the mean (usually m=0) and s the standard deviation

## Slide 23: Random Errors – Normal distribution
We have a measurement, xmeasured = xtrue + e
We’ll assume that systematic errors have been removed from xmeasured by calibration and that e represents random errors only
If we know how e is distributed, we can infer a value for xtrue and its likely error
Normally distributed errors have a probability function
where m is the mean and s the standard deviation

## Slide 24: Normal distribution
A single parameter, s, describes the error distribution so measurements are commonly reported as
m 

## Slide 25: Significance of standard deviation, s
Note that
  68.2% of measurements should fall in the range x 
  95.4% lie in range x 2
  99.7% x 3
  <0.3% have errors greater than 3
So in systems where error is critical (eg safety systems) , you will see references to “3” errors
  Only 0.3% of cases will fall outside the x 3 range

## Slide 26: Non-standard distributions
Although normally distributed random errors are common …
Some situations lead to skewed distributions
  Timing computer programs on a PC
    It’s multi-tasking, so the OS gives some time to housekeeping and other tasks
    These times are sometimes bounded, but generally random and unpredictable
    Thus the measured time is always lengthened by time taken for these tasks
  Weight of a person – skewed
  Price of a share on the stock market
    Chaotic!

## Slide 27: Non-standard distributions
Although normally distributed random errors are common …
Some situations lead to skewed distributions
  The normal distribution is practically zero for values x lying more than a few standard deviations away from the mean
    ie x < m – 3s or x > m + 3s
  Therefore, it is generally not appropriate when there are many outliers, values that lie many standard deviations away from the mean

## Slide 28: Skewed distributions
Mode
  Most common value
Median
  50% of values lie below
  50% of value lie above
Mean
  Arithmetic mean
  Note that there are also other means, eg geometric mean
Normal distributions
  Mode = median = mean

## Slide 29: Skewed distributions
‘Slightly skewed’ distribution
  mode  median  mean
Is the standard deviation meaningful or useful?
  With care!!
  Distribution of values is ‘almost’ normal
  Outliers ( >3 ) are few

## Slide 30: Skewed distributions
Very skewed distribution
  mode  median  mean
Is the standard deviation meaningful or useful?
  No! Outliers ( >3 ) are significant
  Skewness measures, eg kurtosis, Pearson moments, can be used – see your statistics text

## Slide 31: ACCURACY, PRECISION and RESOLUTION

## Slide 32: Terms .. Do not confuse them!
ACCURACY ความแม่นยำ
How close the actual measurement is to the true one
  If voltmeter reads 5.0V when true voltage is 5.5V, then accuracy is 0.5V or 10%
PRECISION (also REPRODUCIBILITY or REPEATABILITY) ความถูกต้อง ความสามารถในการทำซ้ำ
Repeatability or variation in measurement
  If readings vary from 4.5V to 5.5V, then precision is 1V or 20%
RESOLUTION ความละเอียด
Smallest change in value that an instrument can measure
  If the voltmeter displays 5.00, then the resolution is 0.01V or 0.2%
But note that the accuracy may be much worse!!

## Slide 33: Terms .. Do not confuse them!
ACCURACY
How close the actual measurement is to the true one
PRECISION
Repeatability or variation in measurement
RESOLUTION
Smallest change than an instrument can measure
But note that the accuracy may be much worse!!
Resolution
These two are commonly used loosely in English for the same thing!
However, precision has a very specific meaning when talking about scientific measurements

## Slide 34: Some observations
A measurement system can be accurate but not precise, precise but not accurate, neither or both.
eg if an experiment contains a systematic error, then increasing the sample size generally increases precision but does not improve accuracy. The result would be a consistent yet inaccurate string of results from the flawed experiment.
Eliminating the systematic error improves accuracy but does not change precision.
A measurement system is designated valid if it is both accurate and precise.
              Wikipedia, https://en.wikipedia.org/wiki/Accuracy_and_precision

## Slide 35: Valid systems
Be careful with this statement
A measurement system is designated valid if it is both accurate and precise
All measurement systems have errors!
So validity is always related to some acceptable level of error
If 1% error is acceptable, then a valid system must have both accuracy and precision less than 1%

## Slide 36: Accuracy and precision
Target analogy demonstrates the difference well
High accuracy but low precision
  Results are all close to the centre (accurate), but scattered from each other (low precision)
Low accuracy but high precision
  Results are all far from correct one (low accuracy) but close to each other (precise)
Accuracy and precision are commonly used interchangeably when speaking
DO NOT confuse them in your papers, reports or thesis!

## Slide 37: Resolution and precision
Analogue stopwatch
You can estimate the time to 1/10 second
Resolution is 0.1s
Digital stopwatch
You can read the time to 1/100 second
Resolution is 0.01s
but
Both are triggered by a human
  Response time typically ~1/10 second
For both, precision is 0.1s
With modern digital readouts, resolution is often better than precision!

## Slide 38: Targets again Systematic and random errors; precision and accuracy
Low precision, low accuracy
Large systematic error
High precision, low accuracy
Large systematic error remains
High accuracy but precision (repeatability) is still low
High precision, high accuracy
Align the sight to reduce systematic error …
Add a rest to steady the rifle
Align the sight
Add a rest
Images from Dave Tutelman, http://www.tutelman.com/golf/measure/precision.php, 2007

## Slide 39: Reporting results Half the least significant digit rule
Value | Implied error | % error | 
1 | 0.5 | 50% | Guessing is good enough
1.2 | 0.05 | 5% | Rough measurement, field measurements
1.23 | 0.005 | 0.5% | Normal laboratory result
1.234 | 0.0005 | 0.05% | Very careful laboratory work
1.2345 | 0.00005 | 0.005% | Extremely precise laboratory work usually only in standards laboratories
When you write numerical results in your report, you can
Either state the error explicitly: 3.4  0.3 V
or rely on the half the least significant digit rule
3.4V means 3.4  0.05 V

## Slide 40: Reporting results Half the least significant digit rule
Integer results, eg counts
If you write 3042
You imply 3042  0.5
This may not be appropriate if you report the number of people who gave a particular answer in a survey
Report the actual count and explicitly state the estimated error
3042 (margin of error of 3%)
In papers reporting surveys, it is common to state the margin of error in the methods section
  We surveyed 4027 people from a population of ~20,000, so our estimated margin of error is 3%
This is efficient – write actual counts in tables and text –
  you don’t need to add an error to every figure!
but you should repeat the margin of error in the conclusion and the abstract!

## Slide 41: Reporting results Half the least significant digit rule
Integer results
For other measurements, eg
  4024 m2 was planted with taro
Either
    Replace irrelevant digits with 0 and
    state the error explicitly 4020 m2 (1%)
  or
    use scientific notation 4.0 × 103 m2
    implying (4.0  0.05) × 103 m2

## Slide 42: Calibration
Most instruments require calibration because they convert one measure to another
  Digital scale converts pressure (or strain) to weight
  Using pressure gauge or strain gauge, analogue to digital converter, microprocessor
Calibrations determine
  Scaling factors and offsets
  ie parameters in the relation between, eg, weight and strain
  Deviations from linearity
  …
In some cases, calibrations serve to reduce systematic errors
  Small offsets can be measured and subtracted
  Non-linearity can be corrected by using a look up table or function
They also give a good idea of accuracy obtainable
Deviations from curved fitted in calibration exercises indicate accuracy

## Slide 43: Reporting results Half the least significant digit rule
Do not add excess significant digits to your reports!
  Even if you did not explicitly estimate the error, write values that imply reasonable errors!
Generally laboratory work is only accurate to ~1%
Only 2 (maximum 3) significant digits are justified!
  Writing 3.4V  3.4  0.05 V or ~1% error
  Writing 3.42V  3.42  0.005 V or ~0.1% error
    It’s unlikely that your measurement was accurate to 5mV!
    However, it may be accurate to 20mV so 3.42V is reasonable
    but 3.427V  3.427  0.0005 V is definitely not!!
Only special laboratories with high precision equipment routinely achieve < 1% accuracy
  Standards laboratories and some university laboratories

## Slide 44: Reporting results A useful convention
Most workers are reluctant to throw away a 3rd digit
  They don’t want to write 3.4V
  they think their work is a ‘bit’ more accurate and 3.42V is OK
An old convention allowed them to write 3.42V
  Subscript ‘2’ indicates a value which is not certain
  So 3.42V  3.42  ~0.02 V or ~1% error
  Your voltmeter is accurate to 20mV (a modern digital one might well be!) but
    not 5mV (unless you take extraordinary precautions!)
This convention is found in literature about very precise measurements
You should use it!
  It shows your reviewer, examiner and reader that you do understand experimental accuracy even if you did not analyze errors in detail

## Slide 45: Other ‘measurements’
Almost every number has an error associated with it!
but
“I’m studying farm economics, fertilizer is B1000/50kg sack! Where’s the error there?”
  The supplier’s price is fixed
Many actually …
Can you think of some?

## Slide 46: Other ‘measurements’
“I’m studying farm economics, fertilizer is B1000 / 50kg sack! Where’s the error?”
Many actually …
  Variation in price over several years
  Do you get exactly 50kg per sack? how much?
  Farmer wants to apply 80kg/rai ..
    How accurately can he do that?
    He uses a spring scale in the field  10% if he’s very careful!
  How much
    Gets lost in transport,
    Spilt on ground when filling spreading devices
    Spread onto paths, roads instead of crops
    … ?
Overall, this probably means that the effective cost/rai is B1000*80/50 = B1600  20%
rai used here for Thai audience only!
In a paper sent anywhere else, you should use m2!

## Slide 47: Other ‘measurements’
Almost every number has an error associated with it!
but
“I’m carrying out a survey! Where’s the error there?”
  I am just going to ask questions and collect data
Many actually …
Can you think of some?

## Slide 48: Other ‘measurements’
“I’m carrying out a survey! Where’s the error there?”
Many actually …
  Number of people|companies|schools| …. surveyed
  If you survey 80 people and discover
    79 eat very spicy food
    47 own motorcycles
  Your results
    79/80 = 98.75% eat spicy food (you asked 1 farang)
    47/80 = 58.75% own motorcycles (MSU students)
Anything wrong?
  If you only survey 80 people, then your error is at least 1%!!
  Reasonable results
    99% eat spicy food (you asked 1 farang)
    59% own motorcycles (MSU students)

## Slide 49: Errors accumulate!!
If you calculate
  z = x op y
  for any arithmetic operator, op, with x  1%, y 2%
  Then the error in z is (very roughly) 1%+2% or 3%
  It doesn’t matter whether op is +, -, ×, / or ..
Note that the error estimate is an error estimate!
Only one significant figure has any meaning
So your error is 0.5 or 5%
NOT 0.54 or 5.4%!!

## Slide 50: Temperature Accuracy
Generally, you should NOT express any thermometer’s accuracy as %
  temperature  1%, temperature  2%
Report accuracy as  x deg C!
  eg  1 deg C
Reason: Temperature is measured relative to a reference temperature eg 0ºC, 100ºC
So accuracy is referenced to this temperature
But differences in temperature can be expressed as % error
  eg two measurements: T1 = 20 1 ºC, T2 = 70 1 ºC
  So T = T2 – T1 = 50 2 ºC or  4%

## Slide 51: Standards – side note
Use international standards whenever appropriate (unless you are in the United States )
  Measurement units
  SI system
  Incredibly …
    The system has been nearly globally adopted. Only Burma, Liberia and the United States have not adopted SI units as their official system of weights and measures. In the United States metric units are not commonly used outside of science, medicine and the government; however, United States customary units are officially defined in terms of SI units.
    Wikipedia, International System of Units

## Slide 52: Standards
  Measurement units
Absolutely forbidden!
  Imperial units
    feet, inches, miles, pounds, acres, …
    gallons (there are two versions – imperial and US!)
    rai (only Thai understand!)
      use m2 or, possibly, hA = 104 m2
    Tons (imperial version)
      Metric tonne (spelt that way) is OK but possibly confused with imperial ton, so kg are better
    Horsepower – use W or kW

## Slide 53: Standards
  Measurement units
Discouraged
  Non SI metric units
      cm, …
        Use m, mm, ..
          Consistent, fast comparisons with other papers following convention
  Times in minutes, hours, days, ..
    Use seconds when possible
      1 day = 8.64 × 104 s
    But sometimes result looks odd ! So hours, days, .. are OK
  kWh and similar
    Half SI, half customary ..
    Use Joules for preference

## Slide 54: Assignment (assessed 5%)
Find out what instruments you will need for your research
Find out what their accuracy, precision and resolution is
Write a report summarizing what you found
Outline for this report …

## Slide 55: Assignment (assessed 5%)
Outline for your report
  Type of instrument .. What does it measure?
  Machine or device details – manufacturer, model number, date of manufacture, any attachments used
  Physical principle on which it operates
    Very brief (1 or 2 sentences only) + reference
  Calibration method
    Very brief (maximum 1 paragraph)
    Focus on accuracy of calibration!
  Accuracy
  Resolution
  Systematic errors present
    How do you minimize them?
  Random errors
    What causes them?
  What is its precision?
  Summary: overall accuracy and precision

## Slide 56: Assignment (assessed 5%)
Outline for your report
  Use outline to guide your report format
  You should have 10 sections …
In English, but no grammar needed
  Write lists, use bullet points, ….
  If you’re not confident in English
    You can write in Thai and use Google translator or …
You can use this information (after comment and correction) in your thesis!
  It should include detailed experimental method
  Including description of measuring equipment used!
Submit by email to j.morris@auckland.ac.nz
Put ‘RESEARCH METHODS’ in the subject line
Due January 12, 2014
Next lecture : January 18, 2014
Happy New Year!!

## Slide 57: Warning: Google Translator
Google Translator is a good dictionary
  It will generally correctly look up the English equivalent of a Thai word
However
It is very poor at converting Thai sentences to meaningful English sentences!
You must check the English result and make sure that it makes sense!
Tips
  Write very simple, short Thai sentences
  Google can handle these better than long complex ones!
  Good technical writing is simple and short in any language!