## Slide 1: Research Methods: Instrument Accuracy
John Morris
Faculty of Engineering, Mahasarakham University
Computer Science/ Electrical and Computer Engineering,
The University of Auckland
Iolanthe II races off Jomtien, Chonburi Province

## Slide 2: Experiment
GPS Accuracy
Notes
  Earth is circular
  Distance between two points
    Lat1,Lon1 and Lat2,Lon2
  acos(sin(Lat1)*sin(Lat2) + cos(Lat1)*cos(Lat2)*cos(Lon2-Lon1)) *6371
    Excel spreadsheet with formula encoded is available!!
    Latx, Lonx in RADIANS
    Radius of earth ~6371 km
Hypothesis
  What is the accuracy of a GPS position?
  ‘Safe’ expectation ~100m
  Recent GLONASS system: accuracy MAY be as good as 10m

## Slide 3: Experiment – GPS Accuracy
Set GPS to read degrees as 160.xxxxxx
  If you can’t do this, convert deg:min:sec or deg:min.xxxx to degrees
Choose a point that you can recognize from Google Earth
  Choose a reproducible point, eg a corner, recognizable feature
    Being able to repeat the experiment is important
  Locate that point using Google Earth
  Record Lat/Long from Google Earth
Go to that point
Record the GPS reading lat/long
Take at least 30 readings, ~1-2 mins apart
Enter your points data in a spreadsheet
Calculate mean, std dev
Make a histogram showing to distribution of readings
  Make a histogram for 10 points only
  Make another histogram from the 30+ points
Is the distribution normal?
What is (1) Resolution, (2) Precision , (3) Accuracy?

## Slide 5: Experiment – GPS Accuracy - Results
Operation
  GPS receivers measure time of flight from a signal positioned ~20,200 km above the earth
  Usually 6+ satellites are visible at any one time
  Need 4 for accurate position
  ~30 s needed to receive complete data from a satellite

## Slide 6: Experiment – GPS Accuracy - Results
Resolution
  iPad ‘GPS’ program
  Reports lat / long as
  16.247149ºN 103.253024ºE
  Smallest measurable change is 0.000001 deg
  Calculate distance between
    16.247149ºN 103.253024ºE and
    16.247148ºN 103.253024ºE
    0.09 m ???
  Did you see ± 0.09 m ??
Resolution is much smaller than accuracy
Common in modern digital instruments
A
B
C
D

## Slide 7: Experiment – GPS Accuracy - Results
Precision
  Variations in measured distances
  Typically 5-8 m
  Precision is ~ 8m
  Actually good, since satellites are ~20,200km* above the surface of the earth!
  Clock accuracy is better than 1 in 1013 !
Resolution is much smaller than precision
Common in modern digital instruments
19,100km for the Russian GLONASS satellites
A
B
C
D

## Slide 8: Experiment – GPS Accuracy - Results
Accuracy
  Compared with an (approximate) 30m for A-B
  Typically 18-22 m
  Accuracy ~ 10 m
  Actually good, since satellites are ~20,200km above the surface of the earth!
Accuracy is much worse than resolution
Accuracy appears slightly worse than precision
Historical note
  Originally, GPS accuracy was only ~100m
  Accuracy is ~10m now
    Can be affected by atmospheric conditions
A
B
C
D

## Slide 9: Experiment Notes
Important Principle
For any experiment
  Always make multiple measurements of each point
  Reliability is increased by having more points
Important Principle
For any experiment
  Always make multiple measurements of each point

## Slide 10: Experiment Notes
Check measurements AS YOU RECORD THEM!!
Do they match your expectation?
If not, repeat immediately!!
For GPS experiment
  Each measurement at same point should be close to previous one
  Within 10-20m
  If you are not getting the same answer next time
    Check everything
      Recording
      Equipment setting
      Did something change?
        Temperature, wind speed, ..

## Slide 11: Report – First Assignment
Make a short report (in English, grammar-free is OK)
Report structure
  AIM
    What were you trying to demonstrate?
    (here .. Accuracy and resolution of GPS)
  METHODS
    Exactly what did you do?
    What tools did you use?
  RESULTS
    Table of experimental results
    Calculations from those results (distances between points)
    Mention accuracy, precision, resolution!!
  CONCLUSION
    Summarize important results (eg ‘safe’ accuracy of GPS
    ? 3 pages (1 page for table of results!!)

## Slide 12: Experiment Notes
Check measurements AS YOU RECORD THEM!!
Do they match your expectation?
If not, repeat immediately!!
For GPS experiment
  Each measurement at same point should be close to previous one
  Within 10-20m
  If you are not getting the same answer next time
    Check everything
      Recording
      Equipment setting
      Did something change?
        Temperature, wind speed, ..

## Slide 13: Task before next class
Check GPS experiment data
  Check mean, sd
  Check conversions to m
    xi – mean x
    Convert metres … dev * 60 * 1852
    Range for mean deviation … about -10m to +10m
  Now we want to make a HISTOGRAM
  In Excel
    DATA -> DATA ANALYSIS -> Histogram
  Usually DATA ANALYSIS TOOL PAK needs to be downloaded and installed
    Find on web .. Microsoft web site
    Download
    Run installer
  Then ‘DATA ANALYSIS’ tab will appear

## Slide 14: Making a histogram
Makes more flexible plots for your thesis or paper!

## Slide 15: Making a Histogram
If you cannot load the Excel ‘Data Analysis Tool Pak’
Then you can make a histogram yourself
  Not very hard
  More flexible for generating histograms for papers or your thesis!
You can use this procedure for visualizing many types of data
  Scores in a student test
  Measurements of many things, eg speed, time to run 100m, ..
Steps
  Start by copying columns J-L from the GPSVariations sheet
  Make a new sheet and paste them in Columns C-E
  Use the Paste Values option!

## Slide 16: Making a Histogram
In the new (clean) sheet
Note that you will have 3 columns
  Deviations Latitude (North-South), Longitude (East-West) and Distance
  So you can make 3 different histograms
Make sure that Excel has calculated
  COUNT
  MEAN
  SD
  MAX
  MIN
  RANGE
in columns C-E
Follow the example
Put COUNT in row 45

## Slide 17: Making a Histogram
A Histogram shows the FREQUENCY of VALUES in each ‘bin’
A bin is a range of values
In this example, the RANGE is 13
Choose a bin size so that we have 8-20 bins
  More bins if you have more data
Try a bin size of 2
  We will have bins -12, -10, -8, …, -2, 0, 2, 4, … 12
  In bin ‘0’ (‘0’ is the mean) we will count the values from
    -1 < xi <= 1
  In bin ‘2’ , we will count values
    1 < xi <= 3
Make a list of bin START values in column A
  Here it is -13, -11, -9
  Put the minimum -13 in A56
  and “=A56+C$2” in A57
  Copy down (ctrl-D) A57 to A65
  Set the bin CENTRES in column B
  B55 “=A55+C$53/2” and copy down

## Slide 18: Making a Histogram
Carefully copy the formula to B55
Be careful to copy the $s correctly, C$4:C$43, etc .. The $ must be in the right place!
This formula counts values in cells B$4:B$43 IF it is >= bin start (A55) AND < bin end (A56)
Copy the formula from C55 left and down to E68, use ctrl-R
Then you should a set of counts in C55:E68
Now you can make a graph of the data in B55:E68

## Slide 19: Making a Histogram
CHECK what you have down
Note COUNTs in row 70
C70 has “=SUM(C55:C68)”
This should match the count in C45
Matches
So formula was correct
If you had typing error, counts would not match!

## Slide 20: Making a Histogram
To make a single histogram of latitude deviations
Choose B56:C68
Select the chart type you want .. INSERT -> select chart type
Two examples shown here
  Bar chart
    Usual for Histograms
  Freq distribution as graph
Note approximately normal distribution